## Slide 1: Communications Engineering 1
Analog communication systems

## Slide 2: A Baseband Signal
A baseband signal is a signal that occupies the frequency range from 0Hz up to a certain cutoff.
It is called the baseband because it occupies the base, or the lowest range of the spectrum.

## Slide 3: What is modulation?
  Translation of a signal from its baseband to a higher frequency band
  Different signals can be moved to different frequency bands
Modulator
Information
-
bearing signal
Channel
Demodulator
Recovered signal
Modulated signal
Modulating signal
Carrier

## Slide 4: What is modulation?
Signal 1
Signal 2
Signal 3
Frequency
Frequency
Frequency

## Slide 5: Why Modulate?
  Carry multiple signals over a channel
  Move signals to a frequency band where antennas for transmission are of a practical size- The antenna length is proportional to the wavelength of the signal.
  Noise and Distortion Removal

## Slide 6: The carrier signal
Varies some property of the carrier in proportion to the modulating signal
  Amplitude – Amplitude Mudulation (AM)
  Frequency- Frequency Modulation (FM)
  Phase- Phase Modulation (PM)
  Called continuous wave modulation techniques.
Amplitude
Phase
Frequency

## Slide 7: Amplitude Modulation Techniques
Dual sideband suppressed carrier (DSB-SC)
Conventional amplitude modulation (AM)
Single sideband amplitude modulation (SSB)
Vestigial sideband amplitude modulation (VSB)

## Slide 8: Dual sideband suppressed carrier (DSB-SC)
Modulation and Demodulation
Done in class

## Slide 9: AM
Modulation
Done in class

## Slide 10: Envelope Detector
Envelope detector consisting of a diode and a resistor- capacitor combination.

## Slide 11: Envelope Detector
During the positive half-cycle of the input signal, the diode is forward-biased and the capacitor C charges up rapidly to the peak value of the input signal.
As the input signal falls below its maximum, the diode turns off.
This is followed by a slow discharge of the capacitor through resistor R until the next positive half-cycle.
When the input signal becomes greater than the capacitor voltage and the diode turns on again.
The capacitor charges to the new peak value, and the process is repeated.

## Slide 12: DSB-SC Vs AM
DSB-SC has a higher power efficiency compared to, but the demodulation is complex compared to AM :
The basic difficulty associated with the DSB modulation is that for demodulation, the receiver must generate a local carrier that is in phase and frequency synchronism with the incoming carrier.
AM has a lower power efficiency, but a remarkably simple demodulator.
Both techniques utilize twice the bandwidth of the modulating signal.

## Slide 13: SSB and VSB- Bandwidth Efficient Modulation
Will be explained graphically in class

## Slide 14: Frequency Modulation (FM)
Modulation
Done in class

## Slide 15: END