## Slide 1: Field-Effect Transistors
Chapter 6
Boylestad
Electronic Devices and Circuit Theory

## Slide 2
Ch.6 Summary
FETs vs. BJTs
    FETs are voltage controlled devices. BJTs are current controlled devices.
    FETs have higher input impedance. BJTs have higher gain.
FETs are less sensitive to temperature variations and are better suited for integrated circuits
FETs are generally more static sensitive than BJTs.
  Similarities:
    Amplifiers
    Switching devices
    Impedance matching circuits
  Differences:

## Slide 3
Ch.6 Summary
FET Types
JFET: Junction FET
MOSFET: Metal–Oxide–Semiconductor FET
  D-MOSFET: Depletion MOSFET
  E-MOSFET: Enhancement MOSFET

## Slide 4
Ch.6 Summary
JFET Construction
The n-channel is the more widely used of the two.
  The Gate (G) is connected to the p-type material
There are two types of JFETs:
JFETs have three terminals:
  n-channel
  p-channel
  The Drain (D) and Source (S) are connected to the n-channel

## Slide 5
Ch.6 Summary
JFET Operation: The Basic Idea
JFET operation can be compared to that of a water spigot.
The gate controls the width of the n-channel and, therefore, the flow of charges from source to drain.
The source is the accumulation of electrons at the negative pole of the drain-source voltage.
The drain is the electron deficiency (or holes) at the positive pole of the applied voltage.

## Slide 6
Ch.6 Summary
JFET Operating Characteristics
VGS = 0 V, VDS increasing to some positive value
  VGS < 0 V, VDS at some positive value
  Voltage-controlled resistor
There are three basic operating conditions for a JFET:

## Slide 7
Ch.6 Summary
JFET Characteristics: VGS=0V
  Even though the n-channel resistance is increasing, the current from source to drain (ID) through the n-channel is increasing because VDS is increasing.
Three things happen when VGS = 0 V and VDS increases from 0 V to a more positive voltage:
  The size of the depletion region between p- type gate and n-channel increases.
  Increasing the size of the depletion region decreases the width of the n-channel, which increases its resistance.

## Slide 8
Ch.6 Summary
JFET Characteristics: Pinch Off
This suggests that the current in channel (ID) drops to 0 A, but it does not: As VDS increases, so does ID. However, once pinch off occurs, further increases in VDS do not cause ID to increase.
If VGS = 0 V and VDS continually increases to a more positive voltage, a point is reached where the depletion region gets so large that it pinches off the channel.

## Slide 9
Ch.6 Summary
JFET Characteristics: Saturation
At the pinch-off point:
Any further increase in VDS does not produce any increase in ID. VDS at pinch-off is denoted as Vp
ID is at saturation or maximum, and is referred to as IDSS.

## Slide 10
Ch.6 Summary
JFET Operating Characteristics
As VGS becomes more negative, the depletion region increases.

## Slide 11
Ch.6 Summary
JFET Operating Characteristics
ID eventually drops to 0 A. The value of VGS that causes this to occur is designated VGS(off).
Note that at high levels of VDS the JFET reaches a breakdown situation. ID increases uncontrollably if VDS > VDSmax, and the JFET is likely destroyed.
As VGS becomes more negative:
The JFET experiences pinch-off at a lower voltage (VP).
ID decreases (ID < IDSS) even when VDS increases

## Slide 12
Ch.6 Summary
Voltage-Controlled Resistor
The region to the left of the pinch-off point is called the ohmic region.
The JFET can be used as a variable resistor, where VGS controls the drain-source resistance (rd).
As VGS becomes more negative, the resistance (rd) increases.

## Slide 13
Ch.6 Summary
P-Channel JFETs
The p-channel JFET behaves the same as the n-channel JFET. The only differences are that the voltage polarities and current directions are reversed.

## Slide 14
Ch.6 Summary
P-Channel JFET Characteristics
Also note that at high levels of VDS the JFET reaches a breakdown situation: ID increases uncontrollably if VDS > VDSmax.
  The depletion region increases, and ID decreases (ID < IDSS)
As VGS becomes more positive:
ID eventually drops to 0 A (when VGS = VGSoff)
The JFET experiences pinch-off at a lower voltage (VP).

## Slide 15
Ch.6 Summary
N-Channel JFET Symbol

## Slide 16
Ch.6 Summary
JFET Transfer Characteristics
JFET input-to-output transfer characteristics are not as straightforward as they are for a BJT.
BJT:  indicates the relationship between IB (input) and IC (output).
JFET: The relationship of VGS (input) and ID (output) is a little more complicated:

## Slide 17
Ch.6 Summary
JFET Transfer Curve
This graph shows the value of ID for a given value of VGS.

## Slide 18
Ch.6 Summary
Plotting the JFET Transfer Curve
Using IDSS and Vp (VGS(off)) values found in a specification sheet, the transfer curve can be plotted according to these three steps:
1. Solving for VGS = 0 V: ID = IDSS
2. Solving for VGS = VGS(off): ID = 0 A
3. Solving for VGS = 0 V to VGS(off): 0 A < ID < IDSS

## Slide 19
Ch.6 Summary
JFET Specification Sheet
Electrical Characteristics

## Slide 20
Ch.6 Summary
JFET Specification Sheet
Maximum Ratings

## Slide 21
Ch.6 Summary
Case and Terminal Identification

## Slide 22
Ch.6 Summary
Testing JFETs
Curve Tracer
    A curve tracer displays the ID versus VDS graph for various levels of VGS.
Specialized FET Testers
    These testers show IDSS for the JFET under test.

## Slide 23
Ch.6 Summary
MOSFETs
There are two types of MOSFETs:
  Depletion-Type
  Enhancement-Type
MOSFETs have characteristics similar to those of JFETs and additional characteristics that make then very useful.

## Slide 24
Ch.6 Summary
Depletion-Type MOSFET Construction
The Drain (D) and Source (S) connect to the to n-type regions. These n-typed regions are connected via an n-channel. This n-channel is connected to the Gate (G) via a thin insulating layer of silicon dioxide (SiO2).
The n-type material lies on a p-type substrate that may have an additional terminal connection called the Substrate (SS).

## Slide 25
Ch.6 Summary
Basic MOSFET Operation
A depletion-type MOSFET can operate in two modes:
  Depletion mode
  Enhancement mode

## Slide 26
Ch.6 Summary
Depletion Mode Operation (D-MOSFET)
  When VGS = 0 V, ID = IDSS
  When VGS < 0 V, ID < IDSS
The characteristics are similar to a JFET.
  The formula used to plot the transfer curve for a JFET applies to a D-MOSFET as well:

## Slide 27
Ch.6 Summary
Enhancement Mode Operation
(D-MOSFET)
VGS > 0 V, ID increases above IDSS (ID > IDSS)
Note that VGS is now positive
The formula used to plot the transfer curve still applies:

## Slide 28
Ch.6 Summary
p-Channel D-Type MOSFET

## Slide 29
Ch.6 Summary
D-Type MOSFET Symbols

## Slide 30
Ch.6 Summary
Specification Sheet
Maximum Ratings

## Slide 31
Ch.6 Summary
Specification Sheet
Electrical
Characteristics

## Slide 32
Ch.6 Summary
E-Type MOSFET Construction
The Gate (G) connects to the p-type substrate via a thin insulating layer of silicon dioxide (SiO2)
There is no channel
The n-type material lies on a p-type substrate that may have an additional terminal connection called the Substrate (SS)
The Drain (D) and Source (S) connect to the to n-type regions. These n-type regions are connected via an n-channel

## Slide 33
Ch.6 Summary
E-Type MOSFET Operation
VGS is always positive
As VGS increases, ID increases
As VGS is kept constant and VDS is increased, then ID saturates (IDSS) and the saturation level (VDSsat) is reached
The enhancement-type MOSFET (E-MOSFET) operates only in the enhancement mode.

## Slide 34
Ch.6 Summary
E-Type MOSFET Transfer Curve
where:
  VT = the E-MOSFET
  threshold voltage
k, a constant, can be determined by using values at a specific point and the formula:
VDSsat can be calculated using:
To determine ID given VGS:

## Slide 35
Ch.6 Summary
p-Channel E-Type MOSFETs
The p-channel enhancement-type MOSFET is similar to its n-channel counterpart, except that the voltage polarities and current directions are reversed.

## Slide 36
Ch.6 Summary
MOSFET Symbols

## Slide 37
Ch.6 Summary
Specification Sheet
Maximum Ratings
more…

## Slide 38
Ch.6 Summary
Specification Sheet
Electrical Characteristics

## Slide 39
Ch.6 Summary
Handling MOSFETs
  Always transport in a static sensitive bag
  Always wear a static strap when handling MOSFETS
  Apply voltage limiting devices between the gate and source,
  such as back-to-back Zeners to limit any transient voltage.
Because of the very thin SiO2 layer between the external terminals and the layers of the device, any small electrical discharge can create an unwanted conduction.
Protection
MOSFETs are very sensitive to static electricity.

## Slide 40
Ch.6 Summary
VMOS Devices
VMOS (vertical MOSFET) is a component structure that provides greater
surface area.
Advantages
VMOS devices handle higher currents by providing more surface area to dissipate the heat.
VMOS devices also have faster switching times.

## Slide 41
Ch.6 Summary
CMOS Devices
Advantages
Useful in logic circuit designs
Higher input impedance
Faster switching speeds
Lower operating power levels
CMOS (complementary MOSFET) uses a p-channel and n-channel MOSFET; often on the same substrate as shown here.

## Slide 42
Ch.6 Summary
Summary Table