## Slide 1: Communications Engineering 1
Introduction to Telecommunications

## Slide 2: Reference Text
B.P Lathi and Zhi Ding, Modern Digital and Analog Communications Systems, 4th edition, Oxford: Oxford University Press.

## Slide 3: Telecommunications
One of the fastest-growing areas of technology in the world.
Rapid growth.
Businesses and individuals can access information at electronic speed from almost anywhere in the world.
Businesses can provide better services and products to their customers.

## Slide 4: Information
Information is created or used in every human and machine activity
Information is distributed or exchanged in communication
Information in a message is related (inversely) to the probability associated with it
  USA will attack Iraq tomorrow
  Iraq will attack USA tomorrow

## Slide 5: Evolution and Milestones
Mid 1800s: the telegraph, whereby letters were translated into sounds manually, and vice-versa 1857: The Ceylon Telegraph Department is established
1858: The fist telegraph circuit established between Galle and Colombo 1864: James Clerk Maxwell predicts the existence of radio waves 1864: The International Telegraph Union founded, the precursor to today’s International Telecommunications Union (ITU) 1866: The first transatlantic telegraph cable is laid 1876: the telephone is invented 1877: first private line telephones installed for business use
1878 : First commercial telephone exchange opened with 21 subscribers 1879: National Bell Telephone Company formed in the US 1885: American Telephone and Telegraph Company (AT&T) is established in New York City

## Slide 6: Evolution and Milestones
1886: Heinrich Rudolph Hertz demonstrates that rapid variations of electric current could be projected into space in the form of radio waves similar to those of light and heat. 1897: Wireless telegraph is patented by Marconi 1891: The Strowger machine-switching system is patented 1898: Wireless telegraphic connection between England and France established
1901: Marconi successfully transmits radio signal across the Atlantic Ocean from Cornwall to Newfoundland 1902: First bidirectional communication across the Atlantic 1911: The Central Telegraph Office (CTO) building is opened in Colombo Fort 1914: First voice over radio transmission 1925: John Logie Baird demonstrated the transmission of moving pictures, and television was born 1924: Public broadcasting is inaugurated in Sri Lanka 1927: Public demonstration of TV transmission by wire 1932: The International Telegraph Union is renamed as The International Telecommunications Union (ITU)

## Slide 7: Evolution and Milestones
1934 : Federal Communications Commission (FCC) created in the US for telecom regulation 1936 : First coaxial cable installed between New York and Philadelphia for multi-channel telephone systems 1940: Broad band carrier systems are introduced allowing for simultaneous calls over a single pair of wires 1945 : Arthur C. Clarke introduces the concept of using satellites for communications 1946: First commercial multi-channel high frequency microwave radiotelephone system introduced
1960 : Bell Laboratories demonstrates a transUS telephone call by bouncing signals off the moon 1948: First public demonstration of the transistor by Bell Telephone Laboratories 1949 : The ITU becomes a member of the United Nations family of organizations 1955 : Initial trial installation of an electronic switch 1956: First transatlantic cable goes into service with 36 channels between Newfoundland and Scotland
1962: world’s first international telecommunications satellite, Telstar is launched

## Slide 8: Evolution and Milestones
1967: Bell Laboratories introduces a wireless telephone extension 1968: First computer network using packet switching is established at the Lawrence Livermore National Laboratory 1969: Bell Labs creates the UNIX operating system The first network, ARPANET linking four sites is established. ARPANET would become the technical core of the Internet 1973: Development of a common Internetwork Protocol 1973:The first “Mobile Phone” call by Motorola 1974: The term Internet is adopted 1975: Sri Lanka’s first satellite earth station is opened at Padukka
1976 : AT&T installs its first digital switch. 1978: Field trials of the first cellular system, AMPS 1980: International Direct Dialing (IDD) is established in Sri Lanka 1983: The fist cellular system goes into operation in the US. 1985: Sri Lanka subscribes to the SEA-ME-WE submarine cable 1986: First optical fiber cable is laid in Sri Lanka 1987: GSM, the first digital cellular system Standard is made available

## Slide 9: Evolution and Milestones
1988 : The first transatlantic fiber optic cable is installed between USA and England/France with 40,000 channels 1988: The first cellular license is issued in Sri Lanka 1991: The first US digital cellular system introduced 1992 – US introduces the first CDMA-based digital cellular system introduced 1993 – The first digital mobile network is established in the U.S. The first web browser, Mosaic, is introduced.
1995 : 100 million cellular subscribers in the U.S. 30 million users on the Internet worldwide 1996: Email and Internet services established in Sri Lanka 1999: The Internet envelopes the business community as companies scramble to ensure that they are ready to do business via this "World Wide Web". The first release of UMTS (3G) standards is completed. Sri Lanka Telecom installs the 500,000th telephone line in Sri Lanka

## Slide 10: Evolution and Milestones
2000: World’s first 3G/UMTS call
2001: NTT DoCoMo launches the first commercial WCDMA 3G mobile network
2002: SK Telecom in Korea launches the world's first commercial CDMA2000 3G network Mobilkom Austria launches Europe's First UMTS-Network
2003: Korean mobile operator KTF announced plans to begin transmitting TV direct to 3G mobile phones via the CDMA2000 system
2006: SLT installs 1 millionth telephone line in Sri Lanka

## Slide 11: Current Trends
Your first individual mini project.

## Slide 12: Basic Block Diagram of a Communication System.
Information Source
Receiver
Channel
Transmitter
Information
Destination

## Slide 13: Basic Block Diagram of a Communication System.
Source (transmitter) :
Generates the information to be communicated in the form of a signal
Different sources generate information with different characteristics
Source signals need to be analyzed
Transmitter
Receiver
Channel

## Slide 14: Signal Classifications
Continuous time/ Discrete time
Analog/ Digital
Periodic/ Aperiodic
Transient (Energy)/ Eternal (Power)
Deterministic/ Random
Odd/ Even
Explained on the board.

## Slide 15: Frequency domain representation of signals.
Self Study: Revise signals and systems (Semester 3).

## Slide 16: Basic Block Diagram of a Communication System.
Channel or network
The conduit over which the information will be carried
Must be capable of carrying the information generated by the source
Causes loss of information in different ways
Need to analyze the information carrying capacity of channels
  It can be a pair of wires, a coaxial cable, an optical ﬁber, open air, etc.
Transmitter
Receiver
Channel

## Slide 17: Properties..
Channels may carry information
in one direction only (simplex) e.g., radio, TV broadcasts
in both directions sequentially (half-duplex) e.g., normal conversation
in both directions simultaneously (full-duplex) e.g., data transfer between two computers

## Slide 18: Channel Impairments
Attenuation: When a signal, simple or composite, travels through a medium, it loses some of its energy so that it can overcome the resistance of the medium. To compensate for this loss amplifiers are used to amplify (strengthen) the signal.
Distortion (Bandwidth limitations): Distortion is waveform perturbation caused by an imperfect channel response of a communication system.
Eg: Local loop in our telephone network is designed to carry frequencies from 0.3 to 3.4 kHz without significant distortion.

## Slide 19: Channel Impairments
3. Interference: Interference is contamination by other signals from man-made sources, including other transmitters, power lines and machinery, switching circuits, etc.
4. Noise: Noise refers to random signals produced by natural processes both internal and external to a communication system.

## Slide 20: Bandwidth
  The difference between the highest and lowest frequencies that can be transmitted across a transmission medium
  Measured in Hertz (Hz)
  Passband bandwidth: Difference between the upper and lower cutoff frequencies
  Baseband bandwidth: Equal to its upper cutoff frequency
Bandwidth= 2W
Bandwidth= W

## Slide 21: Basic Block Diagram of a Communication System.
Destination (receiver)
Receives the information sent by the source
Loss of information may result in errors
The receiver may try in different ways to correct these errors
Receiver
Channel
Transmitter

## Slide 22: Circuit Switching Vs Packet Switching: Circuit switching
Establishes an end-to-end connection
After circuit is set-up transmitted signals encounter no delays
Technique designed for real-time communication. E.g, voice

## Slide 23: Circuit Switching Vs Packet Switching: Circuit switching
What’s good
–No processing delay at nodes
–Real time communication
What’s bad
–Dedicated resources from end -to -end
–Equal bandwidth in both directions (symmetrical)
Charging is based on duration
The bad points above encouraged the development of packet switching technology

## Slide 24: Circuit Switching Vs Packet Switching: Packet switching
Data is packetized
Each packet has a destination address
Switches look at the address and switch packets
Each packet may take a different route
Non real-time data communication

## Slide 25: Circuit Switching Vs Packet Switching: Circuit switching
What’s good
No dedicated resource. Sharing.
Can have non-symmetrical channels.
What’s bad
Delay at intermediate nodes
Non real-time communication
Charging is based on volume of data transferred
Can have an always – on connection

## Slide 26: References
B.P Lathi and Zhi Ding, Modern Digital and Analog Communications Systems, 4th edition, Oxford: Oxford University Press.
Notes on Elementary Concepts in Telecommunications, Prof. Dileeka Dias, Department of Electronic & Telecommunication Engineering, University of Moratuwa.

## Slide 27: END