## Slide 1: Bioaccumulation and Biomagnification

## Slide 2: Role of Energy
Primary source of energy that drives ecosystems is the sun
Process starts with primary producers that convert inorganic carbon into organic compounds that store energy
Photosynthesis
6CO2 + 6H2O + energy → C6H12O6 + 6O2

## Slide 3: Basic Trophic Levels
Autotrophs
Herbivores
(chemotrophs)
Carnivores
(chemotrophs)
1
2
3

## Slide 4
Food Webs

## Slide 5: Bioaccumulation
Many organic compounds are highly hydrophobic (water hating)
Hydrophobic compounds partition to other phases, such as the plankton, in aquatic systems
The partition coefficient is the equilibrium constant for reaction
chemicalwater == chemicalother phase

## Slide 6: Chemical Pollutants
Humans have been introducing synthetic (man-made) chemicals into the environment.
Some examples are:
  PCBs (polychlorinated biphenyls) widely used in paints, plastics, lubricants up to 1977
  DDT (an insecticide for mosquitos) now banned in many countries
Dichloro-diphenyl trichloroethane

## Slide 7: DDT
DDT was first used in WWII
to protect against diseases
such as typhus and malaria.
It is cheap and effective as
an insecticide – so it began to
be manufactured for home
use.
Before it was banned in 1972
by the EPA for use in
agriculture, 1,350,000,000
pounds of DDT had been
made in North America.

## Slide 11: EFFECTS OF DDT
DDT is found to have estrogenic effects:
  Causes reproductive disorders
  Weakens the shells of eggs (eggs break or do not hatch)
  Can also cause nervous system/ immune system disorders in animals

## Slide 12: DDT – Used as an Insecticide
DDT is used today in such African nations as Zimbabwe and Ethiopia to control mosquitoes and the tsetse fly.
These two insects cause serious diseases, such as malaria and sleeping sickness.

## Slide 13: PCBs
Used widely in products like paints, plastics, etc as softening agents from the 1930’s – 1970’s
Banned in North America in 1977
There are 209 different congeners (different chemical structures)
PCBs interfere with immune function making an organism more susceptible to disease
(ex: cancer)

## Slide 14: Heavy Metals
Heavy metals are metallic elements that are toxic to organisms.
  Levels of lead in the soil have increased due to human activities.
    Lead is not considered safe at any level.
    Many electronics contain lead and must be recycled carefully.
    Lead can cause anemia and nervous and reproductive system damage.

## Slide 15
Heavy metals also bioaccumulate.
  Lead, cadmium & mercury are the most dangerous.
    Lead is not considered safe at any level, it can cause anemia, nervous & reproductive system damage.
    Cadmium is toxic to earthworms & causes many health problems in fish.
    Cadmium causes lung diseases,
    cancer, nervous & immune
    system damage in humans
    (exposure to cigarette smoke).

## Slide 16
Mercury enters ecosystems through burning of fossil fuels,
waste incineration, mining & the manufacture of batteries.
  Coal burning adds 40% of the mercury released.
  Mercury bioaccumulates in the brain, heart & kidneys of many animals (Fish bioaccumulate mercury, adding risk for any organisms eating fish).

## Slide 17: Persistent Pollutants!
Both DDT and PCBs are called “persistent organic pollutants” (POPs)
This is because they take a LONG time to break down
HALF-LIFE = the time it takes for ½ the substance to break down
Half-life (PCBs) = 8 -10 years
Half-life (DDT) = 15 years

## Slide 18: Bioaccumulation
Bioaccumulation is the “build-up of chemicals in living organisms”.
The chemical accumulates because it does not break down easily (decomposers can’t break them down)
The chemicals get stored in fat-cells of organisms and can cause serious problems...
NOTE: Accumulation is measured in parts per million (ppm)

## Slide 20: Bioaccumulation - EFFECTS
How it affects organisms:
  Birth defects
  Failure to reproduce
Amphibians live on both land and in the water.
  Amphibians are sensitive to chemical changes in the environment and are valuable indicators of environmental health.
  Since the 1980s, many of the world’s amphibian species have suffered declines in population.
  There also have been alarming increases in amphibian birth deformities.

## Slide 21
Amphibians, like this frog, have exhibited drastic changes since the 1980s.
Many theories attempt to explain these changes, including drought, increased UV rays, pollution, habitat loss, parasites, and diseases.

## Slide 23
How BIOACCUMULATION affects ecosystems:
  If an important part of the food chain cannot reproduce, the whole food chain is affected.
Keystone species = species that can greatly affect population numbers & health of ecosystem.

## Slide 25: Biomagnification
Biomagnification is
the process where
chemicals accumulate
AND become more
concentrated at each
trophic level of the
food chain.

## Slide 26: Biomagnification
When partitioning concentrates a chemical in one phase that is the food for a higher phase, the chemical can further concentrate as we move up the food chain

## Slide 27: Biomagnification
While partitioning is primarily a chemical process, biomagnification is a complex biological process
Biomagnification factors are empirical

## Slide 31: ORCAS- Biomagnification
The PCB load of orcas (whales) is the highest of any animal in the world.
PCBs concentrate in the blubber of the whale
When the blubber is burned for energy, the PCBs are released into bloodstream (where they affect immune function).
Calves are born with the same PCB level as mother and then obtain more through milk.
PCB’s will affect the reproductive cycles of orcas until at least 2030.
Reproductive success of BC’s resident orcas may be affected until 2030

## Slide 34: Undoing the Damage
Science has found ways of reducing the effects of chemical pollution on the environment...
BIOREMEDIATION
Using living organisms (plants, bacteria) to naturally cleanup chemical pollutants through biodegradation
Chemical-eating bacteria and micro-organisms can break down chemicals into non-toxic compounds!

## Slide 35
Bioremediation is a triple-corners process:
Organisms
Pollutants
Environments
Microorganisms
Plants
Enzymes
Soil
Water
Air
Organic
Inorganic
Solid
Liquid
Gas

## Slide 36: Bioremediation With Plants
Plants can also be used to help trap hazardous wastes such as heavy metals
The plants uptake the metals and trap them in their tissues
Plants also help stabilize by reducing wind and water erosion (that would spread contaminants).

## Slide 37
Metals bioremediation mechanisms
Solubilization
(Bioleaching)
Complexation
(Bioaccomulation)
(Biosorption)
Metal immobilization
Precipitation
- H2S producing bacteria
- Siderophores.
- Metal reduction.
- Exopolysaccharide.
- Lipoproteins.
- Organic acids.
- Siderophores.
- Root exudates.

## Slide 38
Rhodococcus bacteria can
biodegrade PCBs
Bacteria can be used to clean
up oil spills and underground leaks

## Slide 40: Overview and applications
Bioremediation technologies can be generally classified as in situ or ex situ.
In situ bioremediation involves treating the contaminated material at the site while ex situ involves the removal of the contaminated material to be treated elsewhere.
Some examples of bioremediation technologies are bioventing, landfarming, bioreactor, composting, bioaugmentation, rhizofiltration, and biostimulation.

## Slide 41: Overview and applications
Naturally occurring bioremediation: natural attenuation or intrinsic bioremediation
Bioremediation via the addition of fertilizers to increase the bioavailability within the medium: biostimulation
Addition of matched microbe strains to the medium to enhance the resident microbe population's ability to break down contaminants: bioaugmentation

## Slide 42: Overview and applications
Heavy metals such as cadmium and lead are not readily absorbed or captured by organisms. The assimilation of metals such as mercury into the food chain may worsen matters.
Phytoremediation is useful in these situations, because natural plants or transgenic plants are able to bioaccumulate these toxins in their above-ground parts, which are then harvested for removal.

## Slide 43: What Makes Bioremediation a Promising Approach?
permanence
  contaminant is degraded
potentially low cost
  60-90% less than other technologies

## Slide 44: Contaminants Potentially Amenable to Bioremediation

## Slide 46
Biological solution

## Slide 47: Fundamentals of cleanup reactions
Aerobic metabolism
  Microbes use O2 in their metabolism to degrade contaminants
Anaerobic metabolism
  Microbes substitute another chemical for O2 to degrade contaminants
    Nitrate, iron, sulfate, carbon dioxide, uranium, technicium, perchlorate

## Slide 50: Cometabolism
Bacterium uses some other carbon and energy source to partially degrade contaminant (organic aromatic ring compound)
bacterium
corn
starch
CO2 + H2O
contaminant
degradation
products

## Slide 51: A Bright Idea!
Recently, scientists were able to change a gene in these chemical-eating bacteria allowing them to fluoresce (glow) when they are in contact with oil or other chemical pollutants!

## Slide 52: Bioremediation techniques:
A) Soil bioremediation:
(1) In-situ (without excavation).
(2) Ex-situ (with excavation).
Only ex-situ processes allow an efficient optimization of incubation parameters (biostimulation), including:
pH,
Aeration,
Agitation,
Moistening
nutrients,
solvents or surfactants.
In addition to addition of microorganisms (bioaugmentation).

## Slide 53
The ex-situ technique includes:
1- Bioslurry reactor.
2- Biopile.
3- landfarming
Bioslurry reactor.
Biopile.
Biopile.

## Slide 54
1- High density poly ethylene (HDPE)
2- Sump pump to collect leachate
3- Layer of pea gravel
4- Layer of polluted soil to be treated
5- Chopped alfalfa hay to retain moisture
6- Wheels on sprinkler piping system
7- Piping frame, aluminum or PVC pipes with frequent holes, sufficient to allow water, nutrients and bacteria to treat the land farm plot
8- Flexible leachate collection hose
9- Bypass valve that allows leachate to be circulated directly to water distribution tank,
10- Recirculation hose
11- Alken-Murray Bioactivator 2000, bioreactor unit
12- Fresh water supply hoses
13- Pumps for fresh water
14- Treated water hose
15- Water distribution tank
16- Pump for distribution tank

## Slide 55: B- Water and gas bioremediation:
Biofiltration is a process, in which, microorganisms supported on inert materials are used to degrade organic pollutants for air, gas and water bioremediation.
Types of biofilters:
1- Bioscrubbers.
2- Biotrickling filters.
3- Slow sand or carbon filters.

## Slide 56
Bioscrubber filters

## Slide 57: Slow sand or carbon filters
Slow sand or carbon filters work through the formation of a gelatinous layer (or biofilm layer) on the top few millimetres of the fine sand or carbon layer.
This layer contains bacteria, fungi, protozoa, rotifera and a range of aquatic insect larvae (i.e. rotifers).

## Slide 58: Phytoremediation
Phytoremediation is use of plants for accumulation, removal or conversion of pollutants.
Clean up soil and or groundwater
Can remove organics, metals, leftover pesticides, explosives, radioactive waste
Used independently or with other cleanup methods to reduce costs

## Slide 59: Types
Phytoextraction
  Uptake by plants and accumulation in leaves or stem
Phytodegradation
  Plants metabolize contaminants
Rhizodegradation
  Plants promote microbial activity that breaks down contaminants
Phytovolatilization
  Uptake and transpiration

## Slide 61
Approximately 400 plant species have been classified as hyperaccumulators of heavy metals, such as grasses, sunflower, corn, hemp, flax, alfalfa, tobacco, willow, Indian mustard, poplar, water hyacinth, etc.

## Slide 62
The root exudates of these plants play an important role in phytoremediation as it activate the surrounded microorganisms.
Genetic engineering are used as in case of BT protein or insect pheromones producing plants to reduce the use of pesticides.

## Slide 63: Overview
Phytoremediation and self-engineering
Examples of self-engineering at hazardous waste sites
Roles of phytoremediation in ecological engineering

## Slide 64: Strengths and Limitations
Solar driven, self engineering to ensure nutrients and water
Aesthetically
pleasing, eco-restoration
Should be cost effective
Shallow depths of soil or water (rooting depths)
Plants mainly transform contaminants
Long durations and large land areas

## Slide 65: Most Likely Applications
Soil cleanup of oil spills and cyanide
Tree plantations and buffers to control and treat groundwater and surface water contaminants
Wetlands to remove organics from waters
Brownfield stabilization and cleanup
Vegetative caps on landfills
Removal of some metals from soil and water