## Slide 1: Environmental Impact Assessment:
Basic Concepts for Assessing Environmental Impacts

## Slide 2: Review: Definition of EIA
In EIA, the term “impacts” is used instead of “effects of activities.”
What is an impact?
Environmental Impact Assessment is
A formal process for identifying:
  likely effects of activities or projects on the ENVIRONMENT, and on human health and welfare.
  means and measures to mitigate & monitor these impacts

Environment is broadly interpreted: physical, biological, and social.
Notes: Aspects of the environment:
Physical: soil & water resources, air quality
Biological: fauna, flora, ecosystem
Social: human health and welfare, culture, religion, and local values
Or: Economical, social and eco-systemic

## Slide 3: What is an impact?
The impact of an activity is a deviation (a change) from the baseline situation that is caused by the activity.
To measure an impact, you must know what the baseline situation is.
!
The baseline situation is the existing environmental situation or condition in the absence of the activity.
The baseline situation is a key concept in EIA.
More…

## Slide 4: The baseline situation
In characterizing the baseline situation, many environmental components MAY be of interest
Water Quantity, quality, reliability, accessibility
Soils Erosion, crop productivity, fallow periods, salinity, nutrient concentrations
Flora Composition and density of natural vegetation, productivity, key species
Fauna Populations, habitat
Special Key species ecosystems
Env Health Disease vectors, pathogens
The components of interest are those that are likely to be affected by your activity—or upon which your activity depends for its success
Notes: For example, an ecotourism activity might depend on water level in watering holes---but this environmental component is not in fact affected by your activity.

## Slide 5: The baseline situation
The baseline situation is not simply a “snapshot.”
Describing the baseline situation requires describing both the normal variability in environmental components & current trends in these components.
time
Water table
This chart of groundwater levels shows both variability and a trend over time.
Both are part of the groundwater baseline situation.

## Slide 6: Types of impacts & their attributes
Direct & indirect impacts
Short-term & long-term impacts
Adverse & beneficial impacts
Cumulative impacts
The EIA process is concerned with all types of impacts and may describe them in a number of ways
 Intensity  Direction
 Spatial extent  Duration
 Frequency  Reversibility
 Probability
But all impacts are NOT treated equally.

## Slide 7
!
It is ESSENTIAL in EIA to focus on the most significant impacts.
Don’t waste effort & time analyzing and discussing impacts that are less important.
Specifically,

## Slide 8: What is an activity?
ACTIVITY: market access road rehabilitation | ACTIONS: Survey, grading, culvert construction, compaction, etc. . .
a desired accomplishment or output
E.g.: a road, seedling production, or river diversion to irrigate land
An activity is:

Accomplishing an activity requires a set of actions
We are discussing the impacts of activities. What are activities?
A project or program may consist of many activities

## Slide 9: The EIA process
Scope
Evaluate baseline situation
Identify & choose alternatives
Identify and characterize potential impacts of proposed activity and each alternative
Develop mitigation and monitoring
Communicate and document
Phase I: Initial inquiries
Phase II: Full EIA study (if needed)
Our focus!
Understand proposed activities
Screen
Conduct preliminary assessment (if needed)

## Slide 10
Phase 1 of the EIA Process
Screen the activity
Based on the nature of the activity what level of environmental review is indicated?
Conduct a Preliminary Assessment
A rapid, simplified EIA study using simple tools (e.g. the USAID IEE)
ACTIVITY IS OF MODERATE OR UNKNOWN RISK
SIGNIFICANT ADVERSE IMPACTS POSSIBLE
SIGNIFICANT ADVERSE IMPACTS VERY UNLIKELY
ACTIVITY IS LOW RISK (Of its nature, very unlikely to have significant adverse impacts)
ACTIVITY IS HIGH RISK (Of its nature, likely to have significant adverse impacts)
Phase II
Phase I
Understand proposed activity
Why is the activity being proposed?
What is being proposed?
BEGIN FULL EIA STUDY
STOP the EIA process

## Slide 11: Phase 1 of the EIA process: Understand the proposed activity
Understand the proposed activities
Why is the activity being proposed?
What is being proposed?
ALL EIA processes begin with understanding WHAT is being proposed, and WHY.
The question “WHY IS THE ACTIVITY BEING PROPOSED? Is answered with the development objective (D.O.).
“If we don’t understand it, we can’t assess it!”
“building a road”
“increasing access to markets”
We must understand the Development Objective to identify environmentally sound alternatives


Not a D.O.!
Is a D.O.

## Slide 12: Phase 1 of the EIA process: Understand the proposed activity
Understand the proposed activities
Why is the activity being proposed?
What is being proposed?
Once we understand the development objective, we must fully understand WHAT is being proposed.
“Oops. I forgot about the borrow pit.”
This includes associated actions!
PRIMARY ACTIVITY: construction of diversion dam & irrigation canal
ASSOCIATED ACTIONS:
  Survey
  negotiate land tenure
  construct borrow pit
  establish construction camp
  construct temporary diversion structure
  dispose of soil, debris
Notes: Note that the difference between ACTIVITIES and ACTIONS is discussed in

## Slide 13: Phase 1 of the EIA process: Screen the activity
Screen each activity
Based on the nature of the activity, what level of environmental analysis is indicated?
SCREENING is the process of asking a very basic set of questions about the nature of activity.
These questions:
  do NOT require analysis.
  do NOT require detailed knowledge about the proposed sites, techniques or methods
Example screening questions: Does the activity involve:
  Penetration road building?
  Large-scale irrigation?
  Introduction of non-native crop or agroforestry species?
Notes: Are these questions indicative of low-risk or high-risk activities

## Slide 14: Phase 1 of the EIA process: Screen the activity
Screen each activity
Based on the nature of the activity, what level of environmental analysis is indicated?
screening classifies the activity into a RISK CATEGORY:
VERY LOW RISK
VERY HIGH RISK
MODERATE OR UNKNOWN RISK
EIA process ends
Do full EIA study
Do preliminary assessment
The outcome of the screening process determines the next step in the EIA process

## Slide 15: Phase 1 of the EIA process: The Preliminary Assessment
Conduct a Preliminary Assessment
A rapid, simplified EIA study using simple tools (e.g. the USAID IEE)
The purpose of a preliminary assessment is to provide documentation and analysis that:
Screening determines whether the preliminary assessment is necessary
!
Allows the preparer to determine whether or not significant adverse impacts are likely
Allows the reviewer to agree or disagree with the preparer’s determinations
Sets out mitigation and monitoring for adverse impacts

## Slide 16: Phase 1 of the EIA process: The Preliminary Assessment
Typical Preliminary Assessment outline
1. Background (Development objective, list of activities)
2. Description of the baseline situation
3. Evaluation of potential environmental impacts
4. Mitigation & monitoring
5. Recommended Findings
For each activity it covers, a preliminary assessment has 3 possible findings:
  The project is very unlikely to have significant adverse impacts. (EIA process ends)
  With specified mitigation and monitoring, the project is unlikely to have significant adverse impacts
  The project is likely to have significant adverse impacts (full EIA study is required)

## Slide 17: What is mitigation?
Mitigation is. . .
The implementation of measures designed to reduce the undesirable effects of a proposed action on the environment


## Slide 18: To arrive at findings: Identify, Predict and Judge
Identify potential impacts
Judge the significance of potential impacts
Predict potential impacts
Arriving at the FINDINGS in a preliminary assessment requires 3 steps:
Many resources describe the potential impacts of typical small-scale activities.
Determine which potential impacts are likely to become actual, and quantify these impacts to the extent possible.
1
2
3
Determine whether the predicted impacts are indeed significant!
THIS WILL OFTEN DEPEND ON HOW EFFECTIVE THE PROPOSED MITIGATION MEASURES ARE!
Notes: Predicting impacts can involve Quantitative analysis (simulation models, statistical analysis, etc)
It almost always involves qualitative analysis (professional judgment, intuitive reasoning, etc)

## Slide 19
We only proceed to Phase II of the EIA process if Phase I indicates that a FULL EIA STUDY is required
!
Most small-scale activities do not require a full EIA study!

## Slide 20: Phase 2 of the EIA process: The Full EIA study
The full EIA study has very similar objectives and structure to a preliminary assessment.
However, the full EIA study differs in important ways:
A formal scoping process precedes the study to ID issues to be addressed
Analysis of environmental impacts is much more detailed
Alternatives* must be formally defined. The impacts of each alternative must be identified & evaluated, and the results compared.
Public participation is usually required.
A professional EIA team is usually required.
!
!
!
*includes the project as proposed, the no-action alternative at least one other real alternative
!

## Slide 21: Phase 2 of the EIA process: The Full EIA study
With a few additions, the basic outline of the preliminary assessment is the template for the steps involved in a full EIA study:
Scope
Evaluate baseline situation
Identify & choose alternatives
Identify and characterize potential impacts of proposed activity and each alternative
Compare alternatives
Develop mitigation and monitoring
1. Background (Development objective, list of activities)
2. Description of the baseline situation
3. Evaluation of potential environmental impacts
4. Mitigation & monitoring
5. Recommended Findings
Basic steps of the full EIA study
Communicate & Document throughout

## Slide 22
In summary,
The full EIA study is a far more significant effort than the preliminary assessment.

It is reserved for activities for which screening or the preliminary assessment shows that significant impacts are likely.
Phase 2 of the EIA process: The Full EIA study
Notes: The purpose of a Full EIA study is not to find that impacts will not be significant. Its purpose is to allow an informed decision to be made about which significant environmental impacts may be acceptable to obtain a particular development objective. The preliminary assessment cannot serve this function.

## Slide 23: Who is involved in EIA?
Sponsor of the activity (usually commissions/conducts the EIA)
Regulatory agencies/ Review authorities
Broad-based public
Public consultation is usually only REQUIRED for full EIA studies.
However, it is good practice for preliminary assessments because:
  Predicting impacts is FACILITATED by broad-based public consultation; Judging significance is very difficult without it.
  Transparency and accessibility require disclosure to stakeholders
Communities (men & women) Civil society Private Sector

## Slide 24: Making EIA effective
EIA is undertaken early enough to affect project design
Mitigation and monitoring developed in the EIA process is implemented.
To be an effective tool for ESD, EIA must be:
  a integral part of the project development cycle.
  Honest
  Transparent & accessible
The full EIA study must consider real alternatives
Impacts must be assessed honestly.
The EIA products must be clear and accessible to key actors.